## Slide 1: CCNA 200-301, Volume I
Chapter 29
Building a Wireless LAN

## Slide 2: Objectives
Connecting a Cisco AP
Accessing a Cisco WLC
Connecting a Cisco WLC
Configuring a WLAN

## Slide 3: Comparing Connections to Autonomous and Lightweight APs

## Slide 4: Accessing a WLC with a Web Browser

## Slide 5: Accessing the Advanced Configuration Interface

## Slide 6: The Advanced WLC Configuration GUI

## Slide 7: Using WLC Ports
You can connect several different types of controller ports to your network:
Service port: Used for out-of-band management, system recovery, and initial boot functions; always connects to a switch port in access mode.
Distribution system port: Used for all normal AP and management traffic; usually connects to a switch port in 802.1Q trunk mode.
Console port: Used for out-of-band management, system recovery, and initial boot functions; asynchronous connection to a terminal emulator (9600 baud, 8 data bits, 1 stop bit, by default).
Redundancy port: Used to connect to a peer controller for high availability (HA) operation.

## Slide 8: Cisco Wireless LAN Controller Ports

## Slide 9: Using WLC Interfaces
Cisco controllers support the following interface types
Management interface: Used for normal management traffic, such as RADIUS user authentication, WLC-to-WLC communication, web-based and SSH sessions, SNMP, Network Time Protocol (NTP), syslog, and so on. The management interface is also used to terminate CAPWAP tunnels between the controller and its APs.
Redundancy management: The management IP address of a redundant WLC that is part of a high availability pair of controllers. The active WLC uses the management interface address, while the standby WLC uses the redundancy management address.
Virtual interface: IP address facing wireless clients when the controller is relaying client DHCP requests, performing client web authentication, and supporting client mobility.
Service port interface: Bound to the service port and used for out-of-band management.
Dynamic interface: Used to connect a VLAN to a WLAN.

## Slide 10: Cisco Wireless LAN Controller Interfaces

## Slide 11: Connecting Wired and Wireless Networks with a WLAN

## Slide 12: Displaying the List of RADIUS Authentication Servers

## Slide 13: Configuring a New RADIUS Server

## Slide 14: Displaying a List of Dynamic Interfaces

## Slide 15: Defining a Dynamic Interface Name and VLAN ID

## Slide 16: Editing the Dynamic Interface Parameters

## Slide 17: Displaying a List of WLANs

## Slide 18: Creating a New WLAN

## Slide 19: Configuring the General WLAN Parameters

## Slide 20: Layer 2 WLAN Security Type

## Slide 21: Configuring Layer 2 WLAN Security

## Slide 22: Selecting RADIUS Servers for WLAN Authentication

## Slide 23: Configuring QoS Settings

## Slide 24: Configuring Advanced WLAN Settings

## Slide 25: Displaying WLANs Configured on a Controller

## Slide 26: Configuring Management Access from Wireless Networks